## Slide 1
1. The expected noise for flight time is 0.14 seconds. The desired difference to detect is
0.2 seconds. Do a sample size calculation. (Don’t forgot to change “D-Optimal” to “I-Optimal”.)
The instructor will tell you how many blocks will be needed. Create a design matrix for an optimization experiment with the calculated sample size and the indicated number of blocks. (Don’t forgot to change “I-Optimal” back to “D-Optimal”.)
Paper will be treated as a hard-to-change factor. Sort the matrix accordingly.
Save the data table as Helicopter DOE.
We will be dividing into teams to run this experiment. The instructor will show each team how to build the helicopters.
Build the helicopters called for in Block 1 of the design matrix in the data table saved by one of the team members. (The matrix produced by Custom Design will be different for each person.)
Double-check the helicopters against the matrix!
To simulate a shift change, everyone changes manufacturing jobs for Block 2. Block 1 people will provide cross-training as needed before starting Block 2. The new teams will then build the helicopters called for in Block 2.
Double-check the helicopters against the matrix!
Save your design file and give all team members a copy.
Factor | Type | Level 1 | Level 2 | Level 3
Paper | Categorical | Light | Heavy | 
Blade length | Continuous | 3.25" | 4.5" | 5.75"
Stem length | Continuous | 3.5" | 4.0" | 4.5"
Paper clip | Categorical | Small | Large | 
For continuous factors you enter only the low and high levels
Helicopter DOE – Design Phase
We want to maximize the average flight time of paper helicopters dropped from a fixed height. Here are the factors and levels: